Genkidama
Network application protocol definition

# 1. Introduction
This document defines and specifies the Genkidama network application. The document will define the properties of the application protocol in all the fields from the most abstract ones (such as design philosophy, commands in general and semantics) to more specific properties (like per command syntax).
# 2. Protocol minimalist definition
The Genkidama network application protocol is built for communications between GenkidamaH and GenkidamaCD programs through a network. The protocol is designed to sit on top of the TCP transport layer (the protocol itself does not provide any transport level guarantee).
Since the roles of the connected devices are not identical, Genkidama is an asymmetric protocol. The protocol doesn’t explicitly define client and server entities, only host and compute device entities, in most cases though, the host will be the client and the compute device the server. The protocol assumes a stateful connection.
Because of the different types of data that may be transmitted, the protocol works at byte level, bytes might then be interpreted as different data types.
# 3. Protocol requirements
The protocol has to provide an interface wide enough to capture all the use-cases defined for GenkidamaH. The use-cases present some challenges which in turn define some requirements:
- The messages in the protocol need to support dynamic lengths
- The maximum length of the message needs to be big enough for any kind of practical use.
- The messages need to be entirely received before parsing.
- The information conveyed in each message must be self contained, state is not to be used as a tool for translation. For example if dynamic types are being used, information about the type needs to be transmitted too.
- Commands need to be as abstract as possible while staying relatable to use-cases. Flags are to be used to encompass different behaviors.
# 4. Protocol design and commands
The protocol is designed in a hierarchy. The lower level nodes will be more refined commands with narrow scope while the upper levels are about commands in an abstract sense and wide scope. The leaves of the tree are the only real instances of commands.
Because full reception is needed before parsing starts, we need to know the length of the command to decide when we are done reading the command. To achieve this, all dynamic fields in commands are preceded by the length they take, the length is expressed as unsigned int format.

## 4.1 Container node
This node defines how commands are packaged. It defines a frame in which all commands fit. The container contains the information to delimit the command in the byte stream and to allow the parsing of complete commands.
The container node defines two fields:
 The first field is a number (encoded as an 8byte long) that indicates the length of the second field which are the contents of the command
## 4.2 Root node
The root node defines the common properties of all commands, it inherits from the container node.
The root node defines the master field which contains all the information about the command. In this level meta-information is leveraged, i.e. information about the command itself.
The first field is the command type identifier (a byte long), and the second field is the fields of the command type.
## 4.3 Meta node
The meta node specifies the basic syntax for commands that carry meta-information. We say data is meta-info if it doesn’t have to do with the functional aspects of the connection (it does not facilitate a range of use cases), but may be useful to transmit.
The commands derived from the meta node are symmetric in the protocol.
The meta node has two fields and extends from the Root Node:

The first field is the meta-command identifier, the second is the specific fields of the meta-command.
## 4.4 Protocol node
The protocol node extends the root node and defines the properties for the commands that have the control flow defined outside of the very application protocol (these commands are used by some external application to support some features).
The protocol node has 3 fields:
The first field is the command ordinal number (unsigned short format) which tells which command number the issued command is, the second field is the protocol node command identifier, the last field is for the additional fields of the command (command-specific).
# 5. Commands
## 5.1 Meta Commands
### 5.1.1 Command Acknowledgement
This meta command is used by the system implementing the protocol to announce the other end of the connection that a protocol command has arrived and that it has had a positive or negative result when processing. It may also transmit additional information about the result it has had (this is command specific).

The command has three fields:
1. The information about the processed command. Divides up into two sub-fields:
  1. The protocol-command id of the processed command (byte).
  2. The command ordinal number (unsigned short).
2. The result of the processing (0 : OK, >1 : err ; 1 byte).
3. Additional Info:
  1. In case of error, the corresponding additional information to that code (error code dependent).
  2. In case of success completely command depenedent.

* Error codes up to 7f are reserved, command specific codes must be >= 80.
Meta-command id: 0
## 5.2 Protocol Commands
### 5.2.1 Host Commands
### 5.2.1.1 Computation kick command
The computation kick command is used to issue a computation on the compute device by the host.
The computation kick command has 2 fields:
The first field contains a number (unsigned short format) which represents the program that is going to be executed in the compute device. The second field contains the parameters for the program which is sent in list type format.
On acknowledgement:
If OK:
The additional information contains the computation id (2 byte short)
If ERR:
The additional information contains the error code (1 byte):
- 80 : no such program id
- 81 : parameter mismatch
Protocol-command id: 0
### 5.2.2 Compute Device Commands
### 5.2.2.1 Result re-transmission command
The result re-transmission command is used to re-transmit a result of a computation from the compute-device to the host.
The result re-transmission command adds 3 fields:

The first field contains a number (unsigned short format) which represents the id of the computation that was executed in the compute device. The second field (1 byte) indicates whether the program produced any external error (0 = OK, 1 = ERR). The third field contains the result for the program (if OK) which is sent in dynamic type format or UTF-8 encoded bytes with the stack trace of the external error (if ERR).
Protocol-command id: 1
# 6. Formats and additional definitions
## 6.1 Generic formats
### 6.1.1 dynamic type
The dynamic type format is composed by two fields:
The first field is a number in unsigned byte format, which represents the id of the type. The second field is the value of the type. The type id should suffice to parse the content of the second field.
There are various instances of dynamic types, most type ids are left for user definition, some are given in the default implementation.
Type id: does not have
Java type map: DynamicType (interface)
### 6.1.2 List
The list is a dynamic length format which allows to represent a linear collection of ordered data.
The list format is composed of 2*n + 1 fields
The first field indicates how many elements the list has (dynamic type format, this is supposed to be a natural type). The (2*i)th field contains the number (dynamic type format, this is supposed to be a natural type) of bytes that the (2*i + 1)th field has. The (2*i + 1)th field is a dynamic type format.
Type id: 0
Java type map: List<DynamicType>
## 6.2 Simple formats
### 6.2.1 byte
The byte format is composed by a single byte which represent an 8 bit whole number.
Type id: 1
Java type map: byte
### 6.2.2 char
The char format is composed by two bytes which represent a UTF-16 character.
Type id: 2
Java type map: char
### 5.2.3 short
The short format is composed by two contiguous bytes which represent a 16 bit whole number. The format is the same as the char format but gets mapped to other type.
Type id: 3
Java type map: short
### 6.2.4 int
The int format is composed by four contiguous bytes which represent a 32 bit whole number.
Type id: 4
Java type map: int
### 6.2.5 long
The long format is composed by eight contiguous bytes which represent a 64 bit whole number.
Type id: 5
Java type map: long
### 6.2.6 FP32
Single-precision 32 bit float. Expressed in IEEE standard.
Type id: 6
Java type map: float
### 6.2.7 FP64
Double-precision 64 bit float. Expressed in IEEE standard.
Type id: 7
Java type map: double
### 6.2.8 boolean
A byte representing a boolean (7 bits are lost). If true all byte bits to one if false all byte bits to zero.
Type id: 8
Java type map: boolean
## 6.3 Composite formats
These formats exist in order to make transmission of big data efficient (to avoid using List which is very inefficient). All the formats have two fields. For all the formats the first field is a number (in unsigned long format) that expresses the number of elements of the linear collection. The second field is up to the specific format.
### 6.3.1 byte array
This format represents a byte array, the second field of the format is formed of byte formats back to back, as many as indicated in the first field.
Type id: 9
Java type map: byte[]
### 6.3.2 char array
This format represents a char array, the second field of the format is formed of char formats back to back, as many as indicated in the first field.
Type id:10
Java type map: char[]
### 6.3.3 short array
This format represents a short array, the second field of the format is formed of short formats back to back, as many as indicated in the first field.
Type id: 11
Java type map: short[]
### 6.3.4 int array
This format represents an int array, the second field of the format is formed of int formats back to back, as many as indicated in the first field.
Type id: 12
Java type map: int[]
### 6.3.5 long array
This format represents a long array, the second field of the format is formed of long formats back to back, as many as indicated in the first field.
Type id: 13
Java type map: long[]

### 6.3.6 FP32 array
This format represents a float array, the second field of the format is formed of float formats back to back, as many as indicated in the first field.
Type id: 14
Java type map: float[]
### 6.3.7 FP64 array
This format represents a double array, the second field of the format is formed of double formats back to back, as many as indicated in the first field.
Type id: 15
Java type map: double[]
### 6.3.8 boolean array
This format represents a double array, the second field of the format is formed of ceil(n/8) bytes, each bit corresponds to one index of the array. The missing bits are undefined and are padded with whatever value.
Type id: 16
Java type map: boolean[]