Genkidama
Network application protocol definition

# 1. Introduction
This document defines and specifies the Genkidama network application. The document will define the properties of the application protocol in all the fields from the most abstract ones (such as design philosophy, commands in general and semantics) to more specific properties (like per command syntax).
# 2. Protocol minimalist definition
The Genkidama network application protocol is built for communications between GenkidamaH and GenkidamaCD programs through a network. The protocol is designed to sit on top of the TCP transport layer (the protocol itself does not provide any transport level guarantee).
Since the roles of the connected devices are not identical, Genkidama is an asymmetric protocol. The protocol doesn’t explicitly define client and server entities, only host and compute device entities, in most cases though, the host will be the client and the compute device the server. The protocol assumes a stateful connection.
Because of the different types of data that may be transmitted, the protocol works at byte level, bytes might then be interpreted as different data types.
# 3. Protocol requirements
The protocol has to provide an interface wide enough to capture all the use-cases defined for GenkidamaH. The use-cases present some challenges which in turn define some requirements:
- The messages in the protocol need to support dynamic lengths
- The maximum length of the message needs to be big enough for any kind of practical uses.
- The messages need to be entirely received before parsing.
- The information conveyed in each message must be self contained, state is not to be used as a tool for translation. For example if dynamic types are being used, information about the type needs to be transmitted too.
- Commands need to be as abstract as possible while staying relatable to use-cases. Flags are to be used to encompass different behaviors.
# 4. Protocol design and commands
The protocol is designed in a hierarchy. The lower level nodes will be more refined commands with narrow scope while the upper levels are about commands in an abstract sense and wide scope. The leafs of the tree are the only real instances of commands.
Because full reception is needed before parsing starts, we need to know the length of the command to decide when we are done reading the command. To achieve this, all dynamic fields in commands are preceded by the length they take, the length is expressed as unsigned long long format.

## 4.1 Root node
The root node defines the common properties of all commands.
The root node defines the master field which contains all the information about the command. In this level meta-information is leveraged, i.e. information about the command itself.
The first field is the command identifier, and the second field is the fields of the command.
## 4.2 Host node
The host node extends the root node and defines the properties for the commands that the host can send the compute device.
The host node has 2 fields:
The first field is the host command ordinal number (unsigned short format) which tells which command number the issued command is, the second field is for the additional fields of the command.
## 4.3 Compute Device node
The compute device node extends the root node and defines the properties for the commands that the compute device can send the host.
The compute device node has 2 fields:
The first field is the compute device command ordinal number (unsigned short format) which tells which command number the issued command is, the second field is for the additional fields of the command.
## 4.4 Confirmation node
The confirmation node is used to confirm the receiving of a command , whether it has produced an error or not, and the details of the accepting or error.
The confirmation command extends from the root node and adds 2 fields:

The first field is information about the command which includes two sub-fields, the command ordinal number and the command id. The second field is the details about the error or acceptance. This depends on the command to which the confirmation is replaying.
## 4.5 Computation kick node
The computation kick node is used to issue a computation on the compute device by the host.
The computation kick command extends from the host node and adds 2 fields:
The first field contains a number (unsigned short format) which represents the program that is going to be executed in the compute device. The second field contains the parameter for the program which is sent in dynamic type format.
## 4.6 Result re-transmission node
The result re-transmission node is used to re-transmit a result of a computation from the compute device to the host.
The result re-transmission command extends from the compute device node and adds 2 fields:
The first field contains an number (unsigned short format) which represents the id of the computation that was executed in the compute device. The second field contains the result for the program which is sent in dynamic type format.

# 5. Formats and additional definitions
## 5.1 Formats
### 5.1.1 dynamic type
The dynamic type format is composed by two fields:
The first field is a number in unsigned byte format, which represents the id of the type. The second field is the value of the type. The type id should suffice to parse the content of the second field.
There are various instances of dynamic types, most type ids are left for user definition, some are given in the default implementation.
Type id: does not have
### 5.1.2 List
The list is a dynamic length format which allows to represent a linear collection of ordered data.
The list format is composed of 2*n + 1 fields
The first field indicates how many elements the list has (dynamic type format, this is supposed to be a natural type). The (2*i)th field contains the number (dynamic type format, this is supposed to be a natural type) of bytes that the (2*i + 1)th field has. The (2*i + 1)th field is a dynamic type format.
Type id: 0

### 5.1.3 unsigned byte
The unsigned byte format is composed by a single byte which represent a 8 bit natural number.
Type id: 1
### 5.1.4 unsigned short
The unsigned short format is composed by two contiguous bytes which represent a 16 bit natural number.
Type id: 2
### 5.1.5 unsigned long
The unsigned long format is composed by four contiguous bytes which represent a 32 bit natural number.
Type id: 3
### 5.1.6 unsigned long long
The unsigned long format is composed by eight contiguous bytes which represent a 64 bit natural number.
Type id: 4
### 5.1.7 signed byte
The signed byte format is composed by a single byte which represent a 8 bit whole number.
Type id: 5
### 5.1.8 signed short
The signed short format is composed by two contiguous bytes which represent a 16 bit whole number.
Type id: 6
### 5.1.9 signed long
The signed long format is composed by four contiguous bytes which represent a 32 bit whole number.
Type id: 7
### 5.1.10 signed long long
The signed long format is composed by eight contiguous bytes which represent a 64 bit whole number.
Type id: 8
### 5.1.11 FP16
Half-precision 16 bit float. Expressed in IEEE standard.
Type id: 9
### 5.1.12 FP32
Single-precision 32 bit float. Expressed in IEEE standard.
Type id: 10
### 5.1.13 FP64
Double-precision 64 bit float. Expressed in IEEE standard.
Type id: 11
### 5.1.14 char
One byte UTF-8 character.
Type id: 12
### 5.1.15 String
This format represents a string and is of dynamic length.
The format has two fields:
The first field is a number (dynamic type format, it is supposed to be numeric) representing the number of characters to follow. The second field contains the character in char format.
Type id: 13