Genkidama
Network application protocol definition

# 1. Introduction
This document defines and specifies the Genkidama network application. The document will define the properties of the application protocol in all the fields from the most abstract ones (such as design philosophy, commands in general and semantics) to more specific properties (like per command syntax).
# 2. Protocol minimalist definition
The Genkidama network application protocol is built for communications between GenkidamaH and GenkidamaCD programs through a network. The protocol is designed to sit on top of the TCP transport layer (the protocol itself does not provide any transport level guarantee).
Since the roles of the connected devices are not identical, Genkidama is an asymmetric protocol. The protocol doesn’t explicitly define client and server entities, only host and compute device entities, in most cases though, the host will be the client and the compute device the server. The protocol assumes a stateful connection.
Because of the different types of data that may be transmitted, the protocol works at byte level, bytes might then be interpreted as different data types.
# 3. Protocol requirements
The protocol has to provide an interface wide enough to capture all the use-cases defined for GenkidamaH. The use-cases present some challenges which in turn define some requirements:
- The messages in the protocol need to support dynamic lengths
- The maximum length of the message needs to be big enough for any kind of practical uses.
- The messages need to be entirely received before parsing.